## Slide 1: Optimization of Bicycle Suspension Tuning
Bike suspension tuning is more art than science
Applicability of Direct, Stochastic, Population-based algorithms vs. Cyclic Coordinate Descent
2-DoF Dynamical System
& exponential ramp at displacement limits
set by motion rate , 4 regimes
Stochastic terrain incline (SMA smoothing)
8D -
Ground Following – mean distance between tire and ground – corresponds to traction
Ride Comfort (Transmitted Impulse) – RMS of
By Steve Bennett - Taken by Steve Bennett, CC BY 2.5, https://commons.wikimedia.org/w/index.php?curid=7790524
Jeff Robinson AA222 Final Project Presentation June 4, 2019
Problem:
Goal:
Model:
Design Space:
Objectives:

## Slide 2: Optimization of Bicycle Suspension Tuning
Jeff Robinson AA222 Final Project Presentation June 4, 2019
Example Simulation Plots

## Slide 3: Optimization of Bicycle Suspension Tuning
Damping Ratio
Positive sign, except by definition
Quadratic & Count penalties, fixed multiplier
Representatives of each gradient-free type
Direct: Cyclic Coordinate Descent (CCD),
Generalized Pattern Search (GPS) with
basis vectors, Nelder-Mead Simplex (NMS)
Stochastic: Adaptive Simulated Annealing (ASA),
Covariance Matrix Adaptation (CMA)
Population: Particle Swarm Optimization (PSO), Firefly Algorithm
Tested with 3 weightings: [GF, RC] = [1.0, 0.0], [0.5, 0.5], [0.0, 1.0],
640 objective evaluations, 1 iteration of each algorithm
CCD is 4th, GPS is 1st, represent commonly used methods
More sophisticated algorithms require more evaluations, less reliable
Jeff Robinson AA222 Final Project Presentation June 4, 2019
Constraints:
Algorithms:
Results:
Weights | 1.0, 0.0 | 0.5, 0.5 | 0.0, 1.0 | Mean Rank
CCD | 0.0002465 [1] | 3.773 [6] | 6.057 [3] | 3.33
GPS | 0.03780 [2] | 3.495 [4] | 5.781 [1] | 2.33
NMS | 0.04329 [3] | 3.975 [7] | (unstable) | 5.66
ASA | 0.4126 [6] | 3.675 [5] | 6.344 [5] | 5.33
CMA | 0.2389 [5] | 3.221 [1] | 6.215 [4] | 3.33
PSO | 0.1137 [4] | 3.301 [3] | 5.896 [2] | 3.00
Firefly | 0.1137 [4] | 3.277 [2] | 5.896 [2] | 2.66